Wireless Magnetic Door Sensor

DESCRIPTION

Save power design, low power indicated, It is widely used for monitoring and security system, with high reliability, small size, easy installation and operation and strong flexibility. It is

including one transmitter part and one magnetic part, when the door or window is open, it will be

triggered	and	immediately	sends	out	wireless	signal	to	main	alarm	system	to	warning.

Installing place: door, window, draw,cabinet and so on.

SPECIFICATION:

- Triggered distance :<1.5cm

- Working voltage：12V DC, with dry battery model:23A . Low battery voltage about 8V.

- Working current：≤10mA

- Static current：≤5μA

- Working frequency：433.92 MHZ±2KHZ or 315 MHZ

- Transmitting distance：noninterference ≥200m ; indoor about 30~50 m

- Emitting frequency：>10mw

- Frequency tolerance：±0.2MHz

- Operating temperature: indoor -10 ~ 50℃, related humidity ≤ 95%

- Power: standby :0.01W, Alarm :0.09W

- Size: Transmitter part: 90 mm(L)×55 mm(W)×22 mm(H)

Magnetic part: 60mm(L)××15 mm(W)×13 mm(H).	Weight: 50g

INSTALLATION

- Code preset by factory. If not, please follow the following code diagram to play it by clamp

- You should fix the transmitter part on the doorcase, magnetic part on the motion door separately by adhesive, The Led of the transmitter part should near to the magnetic part.

- The distance between the transmitter part and the magnetic part should be no more than 1cm.

- It means OK if the Signal LED flashes for 1 second after installation.

- The signal red LED flash for 1 second to alarm,The low battery green LED lights all along which means batter power is not enough. Please replace the same size new battery

- Antenna is suggested to pull out.