Wireless vibration detector

User manual KI-A031D

DESCRIPTION:

It adopted the detected theory of vibration,. Once it detects any vibration, it will automatically send wireless signal to the control panel for alarm.

It needs to work with alarm panel together, can’t work alone.

It protects in 24 hours to prevent violence (drill, strike, saw etc.) from entering the protected door, window and ceiling and so on. Popular used for window, door, safe guard box, cash box, ATM, night safe guard box, wall, ceiling, device, file cabinet, electrical contacted door and so on. With the high quality sensitive units, it guarantees using life and performance. Long life, high performance rate ratio, low so effectively to prevent from false alarm.

SPECIFICATION:

1. Power supply: Dry battery: A23. 12V DC

2.Max current: 20Ma; Mini current:10mA

3.Pulse output time: .5mS~50mS

- Low battery alarm: Low battery LED is on when it is lower than 8V DC.

- Wireless frequency: 433 MHz

- Transmitting distance：noninterference ≥100m ; indoor about 30~50 m

- Operating temperature: indoor -10 ~ 50℃, related humidity ≤ 95% 9.Chip: 1527,330k resistance

INSTALLATION

1.Remove the battery insulating trip from the detector when you get it

2.Stick the vibration sensor vertically by the double tape on the target which you want to protect .

3.It means OK if the Signal LED flashes when you click it