Wireless Intelligent Roof PIR DETECTOR

Operation Manual

Please read particularly before using it

(1)DESCRIPTION

Adopting advanced digital signal processing technology, Compounding of high precision passive infrared detector and logical digital circuit design, feature intelligent power save, auto- temperature compensation and so on. It emits wireless digital signal to start the control panel for alarm through detecting human being body infrared heat. Nice looking, Reliable and fine quality.

(2) SPECIFICATION

Power supply: 6F22 (normal dry batter) .9VDC (life of battery more than one year)

Working current: 12 MA	Static < 50µA

Wireless frequency:315MHz or 433MHz,Transmitting distance <180 m (open area without interfere) ,indoor: 30~80m.

Respond time choice: one is 6 second(default), the other is 60second. Detecting distance:5m*60°

Detecting range: high 2.4m from ground, covered diameter:7.3m, high 4.5m, covered diameter: 9m

Operating temperature: indoor -10 ~ 50℃, related humidity ≤ 95%

Product size: Φ105*40mm

- INSTALLATION.

1, Installing guide

Code preset by the manufacturer, if not, please following the code diagram (picture 3)to set the eight master codes and four zone code to match the main alarm control panel.

Open the cover(Picture 1), connect the battery, than the detector starts to work. Close the cover, and then install it in proper place (Picture 2)

When the power is on, the LED flashes for about two seconds, the detector will continues to delay for about three seconds or thirty seconds (it depends on protecting time choosing),than it enters the activate situation. If intruder enter protection area. The detector immediately sends out wireless alarm signal.

2. Usage

Walk test: to set the protecting time choosing to 3 seconds by playing pin, simulated as intruder go into the protection area, the LED flashes for about 2 seconds, the detector sends out the wireless signal, meanwhile, the control panel should receive the signal. After walk test, it tested well, please set the protecting time choosing to 30 seconds so as to start to work.

Note: When setting the protecting time, please shut off battery power and press tamper switch once.

- CAUTION

Install the detector to the proper place where intruder must enter.

Do not face the detector to any area where window, lamp-house,heat thing and so on. It is used for indoor,not for outdoor.

When installing, do not drop down or hit the detector so to avoid the internal infrared sensor. Do not touch the sensor lens so to avoid the detecting distance and sensitivity.

Have termly walk test

Round sensitive window

.

(1)	Open cover	(2)Installing height and detecting range

(3)Code diagram and PCB diagram