User’s Manual for LED Wireless Two-Way Keypad

I. Function Features:

- LED lights display, microcomputer intelligent control, stable performance.

- Works with alarm hosts to arm (away) and disarm by password.

- Displays the arm/disarm status simultaneously with the alarm host.

- AV-DC dual-use, high capacity Li-ion battery included; Automatically switches to backup battery power supply mode when power-cut; Automatic data saving when power off; low power alert.

II. Technical parameter:

1. Operating power: 12VDC

2. Operating current: standby current: <10uA

emitting current: <20mA

3. Working condition: Temperature: -10~50℃

Humidity: ＜97%

4. Backup battery: Li-battery

(3.7V / 800mAH, rechargeable)

5. Dimension: 138×88×22（mm）

III. Product Preview:

Front Side

Instructions of LED indication:

1. “Arm Indicator”: Lights on when armed (away) and then off automatically after 8 seconds.

2. “Disarm Indicator”: Lights on when disarmed and then off automatically after 8 seconds.

3. “Low-Power Indicator”: Flashes when low-power and then off automatically after 8 seconds.

4. Program key: Pressing the program key to start the wireless keypad. After pressing this key:

Arm Indicator on indicates the alarm host is in the status of “Armed”,

Disarm Indicator on indicates the alarm host is in the status of “Disarmed”,

IV. Operation and Usage:

【Function】→【Operation Instructions】→Operation explanation

Notes:  1. The wireless keypad will turn off automatically if inactive for 8 seconds.

2. Pressing “*” to start the keypad.

3. A “Di Di DI ” sound indicates wrong pressing.

4. A “Di DI----” sound indicates correct pressing.

- 【Away Arm】：【* + 1+ password + #】 → 4-digits password, the default set before shipment is 8888

2.【Disarm】：【* + 0 + password + #】 →4-digits password, the default set before shipment is 8888.

3.【Change Password】：【*+ 9+ 8888 +# + new password + # + same new password + #】 → The default password before shipment is 8888. (Note: “Di Di DI” indicates wrong operation. This operation should be completed within 8 seconds after power connected)

4.【Panic alarm】：Press the doorbell button on the wireless keypad, the host will give off SOS alarm.

V. Study Operation:

A. The wireless Keypad studies to match the wireless Alarm Host. (To activate/deactivate the function of arm/disarm.)

1. To activate:

1.1. Choose ON for the menu”ARM&DISARM BEEP” on the panel

1.2. Set the Alarm Host to study state ( Find the menu” Add accessory”, and choose ADD REMOTE).

1.3. Now Press *+0+8888+#, TWO times on the wireless keypad. You will see a SUCCESS on the LCD display of alarm host.

2. To deactivate: please follow the deleting instructions of the Alarm Host.

B. The wireless Alarm Host studies to match the wireless Keypad. (To activate/deactivate simultaneous display)

1. To activate:

1.1. Open the back cover of the wireless keypad and press its “Study Button S16” one time

1.2. press the emergency button and hold it 2 seconds on the alarm host to trigger the alarm again, total 2 times to send signal to wireless keypad. Wireless keypad beeps “Di Di Di Di Di” (5 “Di”) to indicate a successful program.

2. To deactivate:

Keep pressing the “Study Button” of the wireless keypad for about 6 seconds and release, a long beep “Di----” from the wireless keypad indicates a successful deleting.