WIRELESS INDOOR PIR DETECTOR WITH PET IMMUNITY

Installation Instructions

1.Product Introduction	2.Main function

It is an intelligent wireless passive infrared detector by a dual - element	-Super micro power consumption design

PIR sensor matching advanced micro power consumption processing technology.	-2 grade detection sensitivities for option

It is very stable, few false alarm and missing alarm. This PIR detector adopts	-Digital pet immunity design up to 20kg

bi-directional temperature compensation technology, which can finish intrusion	(when used with SUNLIT'S pet immunity lens)

detection in a very wide temperature range. Its unique calculation way on pets	-Bi-direction temperature compensation technology

alternative variety can help to avoid false alarm from small animal up to 20kg.	-High capacity battery

Besides, its remarkable performance in anti hot air and faint moving objects	-EDS/anti electric shock/anti mobile phone interference

such as window curtain swaying, can offer very stable detection by 2 sensitivity	-Anti white light

grades. Micro power consumption design makes its battery life expectation up	-With 18 Fresnel lenses with look-down window on 4 planes

to 24 months at least, its function and stability is much better than those detectors	-Well sealed optical parts

selling at similar prices.	-Installation to corner, wall, multi-direction brackets

3.Parameter

Power supply:	3.6V 1/2 AA Lithium battery

Current:	12uA (stand by), 15mA(In alarm),

factory battery can support more than 24 months

Installation height:	1.5m-2.4m

Detection range:	12m*12m 100

Alarm output period:	2s

Temperature compensation: intelligent digital compensation

Sensitivity:	2/3 pulses for option

Anti EMI:	0.1-500MHz/30V/m

Anti white light:	10000 LUX

Alarm output:	EV1527 or PT2262 available

Alarm period:	4 minutes (In USE mode)

Wireless TX distance:	200m in open area

Operation temperature:	-10 /55

Operation humidity:	95% (relatively)

Detection speed:	0.2m/s-3.5m/s

Fireproof protection:	ABS material

Pet immunity:	20kg

Size:	109*65*47mm (H*W*D)

+6m

2m

12m

SIDE VIEW

| - 6m | TOP VIEW |
| --- | --- |

+6m

PET LENS

2m

12m

SIDE VIEW

- 6m

TOP VIEW

4.Installation guide

Choose the best installation position which matches PIR technology and put that onto it . Keep it away from door, window, running machine and hot source

In order to get the best coverage range, detector should be installed at the height of 2.1m, and make vertical adjustment to position 2. In a word,detector can be installed to 4m maximally. Guarantee a wide view angle and no obstacle in front of detector.

X

Detector should not face cold/hot source.

X

Installation foundation should be very stable

Wall surface mount

installation and bracket

Installation should keep away from high-pressure cable.

X

Installation should not face directly to the sunshine.

X

Take care of strong EMI interference.

X

Wrong installation

| wallmount | installation | Hole for surface | Ceiling mount installation and bracket |
| --- | --- | --- | --- |
|  |  | mount installation |  |
| Holefor | bracket | Hole for corner |  |
|  |  | mount installation |  |
|  |  |  | Corner mount installation and bracket |

5. Introduction on internal parts

| TEST/USE mode selection | Alarm indicator |
| --- | --- |
|  | Setting on wireless |
| Detection pulse selection |  |
|  | transmission oscillation |
| Tamper switch | resistor |
| PIR sensor | Setting on wireless |
|  | transmission DATA PIN |
|  | Setting on wireless |
| Wireless transmission module | transmission |
|  | ADDRESS PIN |

Transmission antenna

6. Various settings & walking test

TEST/USE mode switch

When jumper switch is in TEST MODE, detector can detect intrusion signal any time

When jumper switch is in USE MODE, it will take detector 4 minutes to get 2nd alarm signal (This is just to save battery energy, it is the recommended setting)

| TEST |  |  |  |  |  | TEST MODE |  |  | USE MODE |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| USE |  |  |  |  |  |  |  |  | (Energy-saving mode) |

Setting on detector sensitivity pulses

When jumper switch is set to mode of (2 pulses), detector is set to high sensitivity, basically 2 pulses will trigger alarm

When jumper switch is set to mode of (3 pulses), detector is set to low sensitivity, only more than 3 intrusion pulses can trigger alarm

| 3P |  |  |  |  |  | 3 pulses |  |  | 2 pulses |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2P |  |  |  |  |  | (low sensitivity) |  |  | (high sensitivity) |
| PULSES |  |  |  |  |  |  |

LED control

LED ON

walking test

Set detector to TEST MODE, set LED to ON status and closed the front cover, perform horizontal movement in the detection area after LED turns off, you can get the detection status on PIR by the red LED (During alarm, red LED will flash 2 times continuously). This step can confirm whether there is detection dead angle in protected area or not, for PIR is the most sensitive when movement to PIR is horizontal.

In addition, PIR sensitivity can be adjusted properly in different environment installation. Sensitivity is set to 2 grades: 2 and 3 pulses. When 2 pulses is set, detector is with high sensitivity, when 3 pulses is set, detector sensitivity is low relatively, so normally please set it to 2 pulses.

After test is finished, you can turn off alarm LED or keep it as (ON). Strong suggestion: set detector to (USE MODE) and (LED OFF MODE) in order to extend battery life.

LED

LED OFF

7. PCB adjustment

The best detection can be reached by vertical height setting of PCB, suggest installer make the optimum setting on PCB vertical height according to actual environment.

PET- When PCB is set to this mode, detector can get the strongest pet immunity function

NORMAL-When PCB is set to this mode, detector is in the most standard status.

ANTI-CRAWL- When PCB is set to this mode, ambitious crawling intrusion can be avoided effectively, but at this mode, pet immunity function will dropped down slightly.

PET

NORMAL

ANTI-CRAWL

2.1 3.1	5.9	15

PET

2.1m

NORMAL

ANTI-CRAWL

4m

| 3.9 | 6 | 10.4 | 15 |
| --- | --- | --- | --- |
| 1.8 2.7 | 4.8 | 13 |  |
| PET |  |  |  |  |
| NORMAL |  |  |  | 2.1m |
| ANTI-CRAWL |  |  |  | 4m |
| 3.4 |  | 5.2 | 8.7 | 15 |

| 1.5 | 2.3 | 3.7 |  | 8 |
| --- | --- | --- | --- | --- |
| PET |  |  |  |  |
| NORMAL |  |  |  | 2.1m |
| ANTI-CRAWL |  |  |  | 4m |
|  | 2.9 | 4.4 | 7 | 15 |